## Slide 1
A well-preserved historical archive of filters with suspended sediments back to 1975
Long-term ecological research
sites (LTERs) have been measuring water,
nutrient, and particulate fluxes for
several decades by using automatic
samplers.
Total suspended solids (TSS) is one of
the water quality variables measured
at these sites and the filters used to
measure TSS can be preserved for decades
under appropriate conditions.
Our starting point for this project was a collection of filters
and paper archives containing primary data about the amount of water filtered and the mass of the sediments
retained in the filters.
We had to scan hundreds of pages and directly digitize the data to bring this information back to workable formats in the present.
Photo sources

## Slide 2
Long-term measurements of suspended solids have advanced our understanding
about sediment fluxes from headwaters
The most recent studies executed on experimental paired watersheds1,2,3 have examined the role of three main factors on controlling sediment fluxes:
Underlying
geology1
Slope
variability2
Land-use
History2,3
The types of rocks under the soil affect the amount of sediment that is supplied to the stream channels; watersheds with underlying resistant geology have lower sediment yields.
Sites with more irregular surficial topography i.e., slope variability have higher sediment yields and more vulnerable to disturbances.
Sediment
fluxes
There is inconclusive evidence supporting the hypothesis that
changes in land management alone can increase sediment yields from headwater catchments.
Notes: With the aid of statistical models!

## Slide 3
But important questions remain unanswered…particularly those about C fluxes!
Back in the 70’s when the paired watershed studies started most efforts were dedicated to nitrogen and phosphorus fluxes. Yet, C fluxes through these streams were being profoundly affected:
Photo sources
Where are the C sources?
This is
carbon!
This is
carbon!
This is
carbon!
This is
carbon!
This is
carbon!
Watershed 10 (WS10)
before clear-cut 1975
Watershed 10 (WS10)
after clear-cut 1975

## Slide 4
The movement of carbon in streams is strongly linked to the movement of sediments
The dominant view is that C fluxes are controlled by erosion and hence indirectly by other factors affecting the movement of sediments.
Underlying
geology
Slope
variability
Land-use
History
Sediment
fluxes
Carbon
fluxes
The dilution “model”4 originally based on a sample of 19 large rivers was formulated with an interesting caveat: “In spite of the large scatter, one can see that the POC% in the suspended solids generally decreases with increasing TSS concentrations.”
Less scatter for TSS<100 mg/l

## Slide 5
What controls the organic carbon content (%OC) in sediments exported from headwater streams in the Oregon Cascades?
%OC- Total Carbon
in sediments
Total Suspended Solids
(TSS) [mg/l]
In headwater catchments in the Oregon Cascades: 1) TSS is rarely > 100 mg/l 2) organic debris are both vertically and laterally added to the channel , and 3) the streams lack the power to mobilize all particulate inputs:
?

## Slide 6
Source: Bywater-Reyes
et. al., 2018
Our samples come from a paired-watershed study in the H. J. Andrews LTER in the
Oregon Cascades
The H. J. Andrews LTER sits in the
Oregon Cascades Mountains. There,
weathered volcanic rocks are the dominant
underlying geological feature. Lush forests
dominated by pines including Douglas-fir
(Pseudotsuga menziessi) cover most of the
landscape.
In the summer of 1975, the 450+ year old forest on the steep slopes of the experimental Watershed 10 (WS10) was completely removed to study the impacts of logging on
sediment yield and nutrient fluxes (i.e., N, P). An adjacent watershed with similar elevation and underlying geology, Watershed 9 (WS09),was selected as a control watershed for this paired experiment.
Watershed 10 (WS10)
before clear-cut 1975
Watershed 10 (WS10)
after clear-cut 1975
Photo sources

## Slide 7
WS10
Logged in 1975
Logged (WS10) after
Debris flow in 1986
Slope
variability
Land-use
History
Disturbance
Impacts (?!)
We adjusted our conceptual model to account for the particularities of our study sites
Underlying
geology
Sediment
fluxes
Carbon
fluxes
WS09
Old-growth
450-year-old c.a. 1975
The underlying geology of both Watershed 10 (WS10) and Watershed 9 (WS09) was similar (i.e., weathered volcaniclastics)
We compared Logged and Old-growth to include the paired nature of the original experiment.
We had to account for the role of a debris flow in Logged (WS10) and find a proxy for the recovery from that impact over time.
Additionally, the Logged (WS10) site has significantly higher slope variability than the Old-growth (WS09) site.

## Slide 8
The heterogeneity of particle sources adds complexity to understanding what controls the organic carbon content of suspended sediments in headwaters
Stream
channel
Hillslope
Mineral Rich-Carbon Poor
(e.g., mineral soil)
Carbon Rich-Mineral Poor
(e.g., fresh litter inputs)
Instream retention structures
(e.g., large woody debris)
Sediment
particles
Particle subpopulations
Forest
floor
Deep
soil
Source effects on the organic carbon content of stream sediments
The superposition of organic particles from different sources and mobilized by different mechanisms (e.g., surficial erosion, vertical input, lateral input, etc.) suggests the existence of sediment particle subpopulations. These particle subpopulations may carry complex but subtle signals of watershed responses to disturbances and land use history.
Notes: A complex but subtle signal.
Variety of particles, from a statistical point of view this is equivalent to the existence of different subpopulations of particles. But we cannot directly measure this from our filter samples, the amount of TSS we collect on those make more sophisticated chemical analyses complicated, even stable isotopes in some cases.
I included the white “veil” to emphasize that the method does not implies deconvolution of the subpopulations but emphasize multimodality with the built-in assumption that the overall distribution may represent the superposition of different subpopulations.

## Slide 9
We used the novel Beta Regression with Variable Dispersion to model the distribution
of organic carbon content in stream sediments
The “dilution model” does not make
a clear distinction between transport effects (i.e., due to discharge and TSS) and source effects (i.e., due to the variety of sources of organic carbon to the channel).
Statistically speaking, we want to be able to predict changes in the marginal distribution of the carbon content of suspended sediments while assuming the existence of particle subpopulations.
Such a goal can be achieved via beta regression models with variable dispersion5 which, theoretically allow for the effects that the existence of particle subpopulations could have on the overall distribution of the response variable.
Changing mean with
(small) and constant dispersion
Changing mean with
(large) and constant dispersion
Changing mean with
variable dispersion
%OC- Total Carbon
in sediments
Total Suspended Solids
(TSS) [mg/l]
Beta Regression with Variable Dispersion for continuous variables in [0,1]
Transport effects
Source effects
Marginal distributions (envelope)
As a function of discharge (Q)
and Total Suspended Solids (TSS)
As a function of Dissolved Silica (proxy for soil disturbance) and Dissolved
Organic Nitrogen (proxy for effects of land use history)
Notes: I included the white “veil” to emphasize that the method does not implies deconvolution of the subpopulations but emphasize multimodality with the built-in assumption that the overall distribution may represent the superposition of different subpopulations.

## Slide 10
Organic carbon content is larger and more variable in the sediments from the Old-growth site compared with the Logged + debris flow site.
Observed and predicted carbon content (%TC) of suspended sediments from two headwater streams draining an Old-growth forest (WS09-OG site) and a 100%-Logged watershed (WS10-LG site) in the H. J. Andrews Experimental Forest. Predictions are displayed with their corresponding 95% confidence intervals (n = 226, nbootstrap = 500). Model’s predictive performance was corrected for optimism during the bootstrap validation. Kernel density distributions for both the observed and predicted values are plotted along the margins.
These differences in both mean and dispersion suggest that not only the amount of organic carbon being added to the sediments at the Old-growth site is larger, but also that the mechanisms for mobilization of these particles are different as well.

## Slide 11
Disparity plots for the carbon content (%TC) in suspended sediments from from two headwater streams draining an Old-growth forest (WS09-OG site) and a 100%-Logged watershed (WS10-LG site) in the H. J. Andrews Experimental Forest. Dark shaded areas correspond to average kernel densities ± 1 s.d. from boostrap resampling and simulation (nbootstrap = 500). Disparity plots display results for the overall model as well as for transport and source effects calculated while holding their corresponding proxies constant to their long-term medians for the 1984-2014 period (i.e. DSi and DON were held constant to estimate tranport effects and TSS and Discharge were held constant to estimate sourcet effects).
Disparity plots suggest contrasting roles of transport and OM sources in modulating %TC between Old-Growth and Logged sites

## Slide 12
The effect of the superposition of different sources of organic particles is more conspicuous in the Old-growth side, while stronger control by erosion results in larger export of carbon-poor particles from the logged site
Old-growth
Logged + debris flow
Long-term (1984-2015) seasonality and composition of the particulate organic carbon (POC) exported from two headwater streams draining an old-growth forest (WS09-OG site) and a 100%-logged watershed (WS10-LG site) in the H. J. Andrews Experimental Forest. Solid, thick, red lines represent smoothed trends estimated with LOESS regression (smoothing parameter (α)=0.5, the light-shaded region represents 95% confidence intervals around the smoothed trend). The categorical color scale for %TC represents approximately sediment sources identified by Smith (2013): 5-10% surface soils, 11-16% mixed detritus, >17% litter and vegetation. Temporal changes in the proportion of %TC categories are shown in the insets in (a) and (c). Stacked kernel density distributions on the right showing the contribution of different sediment sources to the overall POC yield (b and d, with unstacked versions of the density plots as insets to aid interpretability).

## Slide 17
Biogeochemical and Erosional Controls on Long-term POC Exports from Headwaters
C-Quester’s
Journey
A
Well-preserved archive
of suspended sediment
filters back to 1979
Unknown
Known
Joseph Campbell’s Hero’s journey.
Sediments are measured along with discharge and water chemistry